## Slide 1: STEM Outreach

## Slide 2
Geometric Design​
How to figure out where a road goes​
[Source Brent Moore CC BY2.0 https://www.flickr.com/photos/brent_nashville/8671789592
Notes: Has there ever been a time while you have been driving that you stopped and thought ‘I wonder how they figured out where to put this road’ or even wondered ‘how do they design roads that keep people safe’. Well, today I am here to answer those questions! Today, the topic we will be discussing is Geometric Design.

## Slide 3: Some questions we will cover….
What is geometric design?
Why is geometric design important?
What factors influence geometric design?
How is geometric design conducted for curves?
Notes: This lesson will be over geometric design and it is how engineers figure out how to safely design a road.
So some specific questions we will cover today are: What is geometric design (have you ever heard that term?) Why is geometric design important? What factors influence Geometric Design? How to conduct a Geometric Design for curves?

## Slide 4: What is geometric design?
Did you ever drive along a road and wonder why the curves were the way they were or why the grade is so steep?
  Geometric design determines the layout of the highway so that cars can safely navigate it.
[Source: https://www.publicdomainpictures.net/en/view-image.php?image=184531&picture=rural-road-to-snow-mountains]
Notes: Did you ever drive along a road and wonder why the curves were the way they were or why the grade- or slope - is so steep - Well that is geometric design!
Geometric design determines the layout of the highway so that cars can safely navigate it

## Slide 5: Why is geometric design important?
It ensures safety, comfort and efficiency of all vehicles on our roadways.
  Proper geometric design will help in the reduction of crashes and their severity.
[Source: https://www.popsci.com/uploads/2019/04/22/RACMJSXXIK7BFWBEPV5KGO6TNA-1536x923.jpg]
Notes: Why is geometric design important? Well its all about Safety!…as well as comfort and efficiency Geometric Design allows engineers to figure out the proper speeds, curves, and efficiency of roads to reduce the amount of crashes on the roadways.

## Slide 6: What factors influence geometric design?
There are many factors to consider when designing roads. Some of the main factors in geometric design are:
  Cross section elements
  The gradient
  The intersection
  Sight distance
[Source: https://ebrary.net/182790/engineering/roadway_bridge_cross_design]
Notes: So let’s dive a little deeper and see what factors are important in geometric design. Some things that influence the design of roadways are:
Cross section elements – these deal with the pavement of the roads. They allow for the calculations of the dimensions of the road.
The gradient - how steep of a slope the road can be safely.
Intersections are where two roads cross. They are designed for cars to change roadways safely and depend on the traffic flow.
And finally Sight distance is determined by the drivers ability to see the road ahead.
Each of these will be discussed in further detail.

## Slide 7: Cross section elements
Cross section elements are the features of the roadway that form the effective width of the road. Some of these features include:
  Sidewalks
  Medians
  Bike lanes
  Roadway
[Source: https://nyc.streetsblog.org/wp-content/uploads/2013/08/streetmix_screenshot-1024x513.png]
CTRL + CLICK HERE
Notes: Cross sectional elements are the features of the roadways that form the effective width of the road. Some of these features are the sidewalks, medians, bike lanes, and roadways. You need to know what your road is going to carry in order to design it.

## Slide 8: Gradient
The gradient or grade is the slope of a road or how steep it is.
  It is usually expressed as a percentage (%).
[Source: https://images.immediate.co.uk/production/volatile/sites/21/2021/02/Climbing-on-a-road-bike1-bf2ffba.jpg]
Notes: The gradient is the slope of a road or how steep it is. Gradient is important for the vehicles to be able to drive safely. Engineers use the gradient of roads to help determine speeds and other qualities to ensure that the driver will arrive safely. The gradient is usually expressed in percentages. It needs to be between certain bounds to make sure vehicles can go up hills at a certain speed, and be able to slow down and stop when going down.

## Slide 9: Intersection
[Source: https://nacto.org/wp-content/themes/sink_nacto/views/design-guides/retrofit/urban-street-design-guide/images/intersections-of-major-and-minor-streets/major-minor-streets-2.jpg]
An intersection is a junction where two or more roads intersect.
Some common intersection types include:
  T-intersections
  Crossroads
  Roundabouts
Notes: An intersection is a little more complex. It is a junction between two roads that intersect. An intersection usually has some sort of traffic control whether it be stop signs, traffic light, or yield signs, or it may be a crossroads or roundabout. It depends on the amount of traffic and what kind of traffic
A busy intersection intersections may use stop lights while if there is room and the right amount of traffic Roundabouts are an efficient way for cars to transition onto multiple roads without waiting for a signal.
Crossroads make sure that the driver is aware of any trains crossing at that time.

## Slide 10: Sight distance
Sight distance is how far can the driver see.
It is important to have the line of sight clear of any obstructions (e.g. trees, buildings).
[Source: http://www.landscapes2.org/transportation/circulation/20-Intersections.cfm]
Notes: Our last factor to consider is the Stopping Sight Distance or SSD for short. This is how far a driver can see without obstruction. For safety measures it is important that drivers can see well enough down the road, so that accidents are avoided. Sight distance is important when it comes to safety
A diver must be able to see any other vehicles coming when the road is designed
It is a big safety factor that is included in both horizontal and vertical design

## Slide 11: Safety factors
Engineers must consider other characteristics to ensure safety such as:
  Characteristics of vehicles
  Behavior of the driver
  Traffic characteristics
  Traffic volume
  Traffic speed
[Source: Nick Youngson CC BY-SA 3.0 Pix4free]
Notes: What factors do you think are important to make roads safe?
Some other safety factors that are considered when designing roads are characteristics of vehicles, behavior of drivers, traffic, traffic volume, and traffic speed.
Each of these are used to ensure that the roadways are safe. They are all considered when designing the road and will go into further detail of each in the presentation.

## Slide 12: Vehicle characteristics
[Source: https://nacto.org/publication/urban-street-design-guide/design-controls/design-vehicle/]
Designers use a design vehicle to set characteristics of the roadway, this is usually passenger cars for most local roads, but trucks are taken into consideration for highway design (e.g., entrance ramps).
[Source: https://www.youtube.com/watch?v=GftnaCDu78k]
Notes: When designing roads it is important to consider what kind of vehicles will be taking this road. When engineers design a road they consider that there will likely be more passenger cars driving than large trucks, but they must keep those trucks in mind.
Why do you think larger vehicles be considered differently than cars?
Trucks having a more difficult time on roads that are smaller or in more populated areas. Take a look at this picture – it is very hard for this truck to make a turn on a local road
All vehicle types must be considered when designing a road. Usually, passenger cars control local roads, but larger trucks control most of the main roads.

## Slide 13: Behavior of the driver
Driver behavior is the intentional and unintentional actions that a driver performs while operating a vehicle, such as:
  Distracted Driving
  Speeding
  Tailgating
Notes: The behavior of drivers is a little harder to pin down than the vehicle characteristics. The human error that can occur much be accounted for. Intentional and unintentional actions like speeding, distracted driving, and tailgating are still approximated and accounted for when designing roadways.

## Slide 14: Traffic characteristics
Traffic characteristics describes the different types of vehicles present and expected to use the roadway.
[Source: https://www.esranet.eu/storage/minisites/esra-topics-02banner.png]
Notes: Traffic characteristics go beyond just vehicles to include pedestrians, cyclists, etc …For example, it a road is to have cyclists there must be a way for them to ride safely.
Each of these must be considered in road design.
They all may use the road if they aren’t considered, then there will more likely be accidents or other incidents happening. Have you ever seen a road that is not safe to walk on – there are some roads designed with pedestrians in mind (by providing sidewalks) and some that are not.

## Slide 15: Traffic volume
Traffic volume is the number of vehicles that are present on the roadway during a period of time.
The volume can change throughout the day.
[Source: https://qph.cf2.quoracdn.net/main-qimg-fcedb015837968eb1fe379abcd3968bc-lq]
Notes: Traffic volume is also very important and it can change throughout the day.
Why do you think the traffic volume changes with the time of day?
This is due to the schedules of our society being very similar. Most people have to go to work at a similar time, eat at a certain time, and go home at a certain time
At those times the traffic will increase and it must be accommodated for to ensure people travel safely

## Slide 16: Traffic speed
Traffic speed is the measure of how fast vehicles are traveling on the roadway.
Speed limits are typically set based on the roadway characteristics.
[Source: https://www.motorbiscuit.com/wp-content/uploads/2021/09/speed-limit-sign-1024x762.jpg]
Notes: Speed is another important factor to consider to make sure the roads are safe.
The speed of roads is decided based on the surrounding areas and the road type
If there are more intersections or curves, then the speed will be slower than something like an interstate with on and off ramps.

## Slide 17: Curves
Horizontal and vertical curves are designed so that the car stays on the road.
  Vertical – so that car maintains downward forces - so tires stay on road.
  Horizontal – so that car can make turn without sliding to the side.
Notes: So now we know some things to consider in roadway design – but how do you actually design a road? Today we are just going to focus on the design just for the horizontal and vertical curves – and not worry about the other considerations for now.
Ok – so now let’s define curves. A vertical curve is where a car can go up and down safely without leaving the ground. – you don’t want a roller coaster road! You need to maintain gravity so that the tires stay on the road and the driver can stop and steer
Horizontal curves are designed so that the car can make the bend in the road without too much horizontal force. If the bend is too sharp depending on the speed of the car the horizontal force can overcome the friction from the tires on the road and allow the car to slide off.
All of these depend a lot on the speed of the car and the friction on the road (which is why you need to slow down when it is icy – the roadway is not designed with ice in mind).

## Slide 18
Notes: This is an example of a curve that is too sharp in the vertical and horizontal direction. The car loses traction and goes off the road. What would you change?

## Slide 19
Notes: This is the correct way the curve should be based on the speed of the car.

## Slide 20: Vertical curves
A vertical curve connects two different grades along the roadway.
There are two types of vertical curves:
  Crest Vertical Curve: where the initial grade is greater than the final grade (like on a hill).
  Sag Vertical Curve: where the initial grade is smaller than the final grade (like in a valley).
Notes: So let’s get a little more into vertical curves. A crest vertical curve is used at the top of a hill and a sag vertical curve is the like a valley. Think of these as a crest curve being a frowny face and and a sag curve being a smiley face

## Slide 21: Vertical curve elements
The factors that define a vertical curve include:
  Curve length (L)
  Elevation of designated point, such as PVC, PVT, etc.
  Initial and final grade (G1 and G2)
  Sight distance (S)
  Rate of curvature (K)
[Source: https://media.cheggcdn.com/media%2F3ef%2F3ef947db-4223-493a-880e-d3ce6c828c2b%2Fphp0piZFb.png]
Notes: The factors that define a vertical curve include the curve length (L), elevations (PVC and PVT), initial and final grade (G1 and G2), site distance (S), and rate of curvature (K). All of these are factors that can be found with different equations and tables.

## Slide 22: Vertical curve calculations
Curve length (L) = K*A,
  where A =|G1 - G2| (i.e. the absolute value of the difference of initial and final grades)
To calculate the length of vertical curves, we use K values from tables depending on whether we have a Crest curve or Sag curve and the design speed.
Notes: So let’s look at the equation.
The formula to find a curve length (L) is K times A where A is the absolute value of the difference in the gradients.
K is found from a table that takes into consideration the sight distance and speed as well as how much g force is needed to keep the car on the road. It is different for Crest or Sag curves.

## Slide 23: Vertical curve example
What is the proposed curve length of a crest curve with grades G1 = 3% and G2 = -1.5% and design speed of 40 mph?
  L = K*A = 44 * | 3% - (-1.5%) | = 198 ft
What is the proposed curve length of a sag curve with grades G1 = -2% and G2 = 1% and design speed of 45 mph?
  L = K*A = 79 * |(-2) - 1| = 237 ft
Notes: So let’s take a look at an example
Say we had a crest curve with grades G1 = 3% and G2 = -1.5% and design speed of 40 mph
Looking at the table for 40 mph we find that K is 44. There for the length of the curve is 44 times the absolute value of 3%- negative 1.5%. Which is 198ft. That is how long the circular segment of the curve needs to be.
Ok another example
What is the proposed curve length of a sag curve with grades G1 = -2% and G2 = 1% and design speed of 45 mph?
Looking at the sag table we see K is 79 so the length of the curve is 79 times the absolute value of -2%- 1%. Which is 237ft.
Pretty simple huh? Well these are simple cases but you can see how it works to find the curve length.

## Slide 24: Horizontal curves
A horizontal curve provides a transition between two tangent sections.
Examples of horizontal curves:
  Simple Circular Curve
  Reverse Curve
  Compound Curve
  Spiral Curve
Notes: For horizontal curves Tangent lines are drawn to connect two roads together to make one road. The road will have curve and it is the engineers job to find the safest curve based on speed

## Slide 25: Horizontal curve elements
The factors that define a simple horizontal curve include:
  Curve Radius (R)
  Tangent Distance
  Degree of curvature
  Central Angle
  Superelevation (banking)
Notes: The factors that define a simple horizontal curve include,
  Curve Radius
  Tangent Distance
  Degree of curvature
  Central Angle
  Superelevation (banking)
  All of these values are used to figure out the different elements of the curve based on the tangent lines.

## Slide 26: Horizontal curve calculations
To calculate the length of horizontal curves, we select a radius value from a table based on the design speed.
From the proposed road diagram, the angle that forms between the tangents (∆) is also required to calculate the length.
The formula is: L = (𝜋/180)*𝑅*∆
Notes: To calculate the length of horizontal curves, we select a Radius value from a table based on the design speed
We also need the angle between the tangent segments or delta
Then the formula for the length is L = (pi/180)*R*delta

## Slide 27: Horizontal curve example
What is the proposed curve length of a horizontal curve with a design speed of 40 mph and a ∆ of 35° given a maximum superelevation rate (e) of 6%?
  L = (𝜋/180)*𝑅*∆ = (𝜋/180) * 485 * 35 = 292.3 ft
What is the proposed curve length of a horizontal curve with a design speed of 35 mph and a ∆ of 60° given a maximum superelevation rate (e) of 4%?
  L = (𝜋/180)*𝑅*∆ = (𝜋/180) * 371 * 60 = 388.5 ft
Notes: So let’s do some more examples.
What is the proposed curve length of a horizontal curve with a design speed of 40 mph and a ∆ of 35° given a maximum superelevation rate (e) of 6%?
Well let’s look at the table with the superelvation of 6% and find the row with a design speed of 40 mph. It says the Radius is 485 ft.
So our length is (pi/180)*485*35 = 292.3ft
Another example
What is the proposed curve length of a horizontal curve with a design speed of 35 mph and a ∆ of 60° given a maximum superelevation rate (e) of 4%?
Well let’s look at the table with the superelvation of 4% and find the row with a design speed of 35 mph. It says the Radius is 371 ft.
So our length is (pi/180)*371*60 = 388.5ft
Again this is a simple example – but you can see how engineers can determine how long the curves need to me when designing a road – cool!

## Slide 28: Measurements within geometric design
When designing curves in geometric design, the unit of measurement is Stations.
Stations are measured in the horizontal plane, and they represent every hundred feet in distance.
A station measurement is written as an addition of coordinates.
  E.g. 12,465 ft = 124+65 stations
Notes: Stations are used as a way for points on the road to be understood and calculated easier

## Slide 29
Notes: Now Let’s hear from a real engineer about how he designed a new roadway with some of those other factors involved

## Slide 30: Now go out there and design some roads!
[Source https://en.wikipedia.org/wiki/Geometric_design_of_roads#/media/File:Autovia_olivar.jpg]
Notes: Now go out and design some roads!